## Slide 1: Review
TINKERCAD CORE CODING BLOCKS

## Slide 2
Uses I/O pin as a digital input.
Returns either:
  0 (LOW, 0v)
  1 (HIGH, 5v)
pins as inputs
Uses I/O pin as an analog input.
Returns values in a range between:
  0 (LOW, 0v) – 1023 (HIGH, 5v)
Only pins A0-A6 can be used for analog reads

## Slide 3
Changes the voltage on a particular IO pin. (pin being used as an output)
Can be set to:
HIGH (5v)
LOW (0v)
different outputs
Allows us to print a message to the Serial Monitor.
Essential for debugging
Can print words (strings) or numeric values

## Slide 4
Puts a value into a variable
Also creates the variable if it hasn’t been used before
If it currently has a value, the old one is discarded to make room for the new one.
using variables
Increases the value of a variable by addition
Adds the number entered (argument) and the existing value together, and stores that new value in the variable.
Actual variable block.
Allows us to refence the value stored in the variable